| Rider: | Bike: |
| --- | --- |
| Tech Inspection For Track Days |
| Check | Things that need to be wired |
|  | Engine oil drain plug |  |
|  | Engine oil filler cap |  |
|  | Bolts to Check |  |
|  | Brake caliper bolts |  |
|  | Clip-on or handlebar bolts |  |
|  | Front axel Pinch bolts |  |
|  | Rear axle |  |
|  | Front axle |  |
|  | Check the rearset or footpeg bolts |  |
|  | Sight Checks |  |
|  | Check the tires for wear |  |
|  | Look for fluid leaks from the engine (oil, coolant). |  |
|  | Fork Seals |  |
|  | Look for damaged or leaking lines, brake, clutch fuel. |  |
|  | Check brake pad wear |  |
|  | Brake fluid, front and rear level |  |
|  | Clutch fluid level |  |
|  | Engine oil level |  |
|  | Engine coolant level |  |
|  | Other things to Check |  |
|  | Tire Pressure <- Very Important |  |
|  | Throttle Action; The throttle grip should “snap” back after it is opened and is let go, make sure you check the throttle action at both right and left full lock as well. |  |
|  | Throttle slack; How much does the grip move before the throttle opens? |  |
|  | Chain Adjustment <- VERY Important |  |
|  | Front brake/Clutch lever position Make sure the levers are at a comfortable position for the rider |  |
|  | Rear brake; Check to see if the foot pedal is in the right position for the rider |  |
|  | Fuel level <-Sucks to take a crash truck ride because you ran out of gas |  |
|  | For Street Bikes; Remove mirrors from the bike, if you cannot do that, tape the glass surfaces Tape up your headlight, taillight, and turn signals. In the event of a crash the tape will keep all of the small pieces from covering the track, which save clean up time. If you can you should also disconnect the headlight, as the tape could get melted onto the headlight lens causing a gooey mess to get off later. |  |